## Slide 1: Unit III VLSI CIRCUIT DESIGN PROCESSES
Topics
VLSI design flow
MOS layers
Stick diagrams
Design Rules and Layout
2 um CMOS design rules for wires
Contacts and Transistors
Layout diagrams for NMOS and
CMOS inverters and gates, Scaling of MOS circuits

## Slide 2: VLSI Design of approach of IC
62/038/2015

## Slide 3: Layer Types
p-substrate
n-well
n+
p+
Gate oxide (thin oxide)
Gate (polycilicon)
Field Oxide
  Insulated glass
  Provide electrical isolation

## Slide 4
Stick diagram
Encodings for a simple single metal nMOS process
BROWN
COLOR | STICK ENCODING MONOCROME | LAYERS | MASK LAYOUT ENCODING MONOCROME | CIF LAYER
GREEN RED BLUE BLACK GRAY nMOS ONLY YELLO WnMOS ONLY | NOT APPLICABLE | n- diffusion n+active Thniox Polysilicon Metal 1 Contact cut Overglass Implant Buried contact |  | N D NP N M N C N G NI NB

## Slide 5
Stick Diagrams
Metal
poly ndiff
pdiff
Can also draw in shades of gray/line style.
Buried Contact
Contact Cut

## Slide 6: Stick Diagrams
VLSI design aims to translate circuit concepts onto silicon.
Stick diagrams are a means of capturing topography and layer information using simple diagrams.
Stick diagrams convey layer information through colour codes (or monochrome encoding).
Acts as an interface between symbolic circuit and the actual layout.
Does show all components/vias.
It shows relative placement of components.
Goes one step closer to the layout
Helps plan the layout and routing

## Slide 7: Stick Diagrams
Does not show
  Exact placement of components
  Transistor sizes
  Wire lengths, wire widths, tub boundaries.
  Any other low level details such as parasitics..
Does show all components/vias.
It shows relative placement of components.
Goes one step closer to the layout
Helps plan the layout and routing

## Slide 8: Stick Diagrams – Some rules
Rule 1.
When two or more ‘sticks’ of the same type cross or touch each other that represents electrical contact.
Rule 2.
When two or more ‘sticks’ of different type cross or touch each other there is no electrical contact.
(If electrical contact is needed we have to show the connection explicitly).

## Slide 9: Stick Diagrams – Some rules
Rule 3.
When a poly crosses diffusion it represents a transistor.
Stick Diagrams
Note: If a contact is shown then it is not a transistor.

## Slide 10: Stick Diagrams – Some rules
Rule 4.
In CMOS a demarcation line is drawn to avoid touching of p-diff with n-diff. All pMOS must lie on one side of the line and all nMOS will have to be on the other side.
Stick Diagrams

## Slide 11
5 V
Dep
Vout
Enh
0V
0 V
Vin
5 v
NMOS INVERTER

## Slide 12: NMOS-NAND

## Slide 13: NMOS-NOR
6/3/2015
222

## Slide 14: NMOS EX-OR
6/3/2015
223

## Slide 15: NMOS EX-NOR
6/3/2015
224

## Slide 16: PMOS-INVERTER
6/3/2015
225

## Slide 17: PMOS NAND
6/3/2015
226

## Slide 18: PMOS-NOR
6/3/2015
227

## Slide 19: Sticks design CMOS NAND:
Start with NAND gate:
6/3/2015
228

## Slide 20: NAND sticks
VSS
6/3/2015
229
VDD
a
out
b

## Slide 21
Stick Diagram - Example
OUT
B
NOR Gate
A
6/3/2015
230

## Slide 22
Stick Diagram - Example
Power
Ground
C
B
Out
A
6/3/2015
231

## Slide 23: 2 I/P OR GATE
6/3/2015
232

## Slide 24: 2 I/P AND
6/3/2015
233

## Slide 25
6/3/2015
234

## Slide 26: Y=(AB+CD)’
6/3/2015
235

## Slide 27: Y=(AB+CD)’ STICK
6/3/2015
236