## Slide 1: PART-1 NUMBER SYSTEMS

## Slide 2: Digital System
Takes a set of discrete information inputs and discrete internal information stem state and generates a set of discrete information outputs.
Discrete
Inputs
Discrete Information Processing System
ystem State
Discrete
Outputs

## Slide 4: Digital Computer Systems
Digital systems consider discrete amounts of data.
Examples
26 letters in the alphabet 10 decimal digits
Larger quantities can be built from discrete values: Words made of letters
Numbers made of decimal digits (e.g. 239875.32)
Computers operate on binary values (0 and 1)
Easy to represent binary values electrically Voltages and currents.
Can be implemented using circuits
Create the building blocks of modern computers

## Slide 5: A basic organization of a digital computer

## Slide 6: Types of Systems
With no state present
  Combinational logic system
  Output = Function (Input)
With state present
  State updated at discrete times (e.g. once per clock tick)
Synchronous sequential system
  State updated at any time Asynchronous sequential system

## Slide 7: Example : Digital Counter
Inputs
Outputs
State
: Count Up, Reset
: Visual Display
: “Value of stored digits
Is this system synchronous or asynchronous?
0 | 0 | 1 | 3 | 5 | 6 | 4
(e.g., Odometer)
UP RESET

## Slide 9: Signals
orma ion varia es mappe ysica
ies
In digital systems, the quantities take on discrete
values
  Two-level, or binary, values are the most prevalent values in digital systems
  Binary values are represented abstractly by digits 0 and 1
Signal examples over time:
Analog
Asynchronous
(Time) Synchronous

## Slide 10: Physical Signal Example
Voltage
OUTPUT
1.0
INPUT
Threshold
Region
Other physical signals representing 1 and 0
CPU
Disk
CD
Dynamic RAM
Voltage
Magnetic field direction Surface pits / fight Charge

## Slide 11: Number Systems
Decimal Numbers
  What does 5,634 represent?
  Expanding 5,634:
5 x 10* = 5,000
+ 6 x 102 = 600
+ 3 x 101 = 30
+ 4 x 100 = 4
-2 5,634
What is “10” called in the above expansion?
The radix.
What is this type of number system called?
Decimal.
What are the digits for decimal numbers?
0, 1, 2, 3, 4, 5, 6, 7, 8, 9.
What are the digits for radix-r numbers?
0, 1, ..., r-1.

## Slide 12: Understanding Decimal Numbers
Decimal numbers are made of decimal digits: (0,1,2,3,4,5,6,7,8,9)
But how many items does a decimal number represent?
8653 = 8x103 + 6x102 + 5x101 + 3x100
What about fractions?
97654.35 = 9x104 + 7x103 + 6x102 + 5x101
+ 4x100 + 3x10-1 + 5x10-2
In formal notation -> (97654.35)10
Why do we use 10 digits, anyway?

## Slide 13: Understanding Octal Numbers
Octal numbers are made of octal digits: (0,1,2,3,4,5,6,7)
How many items does an octal number represent?
(4536)8 = 4x83 + 5x82 + 3x81 + 6x80 = (1362)10
What about fractions?
(465.27)8 = 4x82 + 6x81 + 5x80 + 2x8-1 + 7x8-2
Octal numbers don’t use digits 8 or 9
Who would use octal number, anyway?

## Slide 14: Understanding Binary Numbers
Binary numbers are made of binary digits (bits):
0 and 1
How many items does an binary number represent?
(1011)2 = 1x23 + 0x22 + 1x21 + 1x20 = (11)10
What about fractions?
(110.10)2 = 1x22 + 1x21 + 0x20 + 1x2-1 + 0x2-2
Groups of eight bits are called a byte
(11001001) 2
Groups of four bits are called a nibble.
(1101) 2

## Slide 15: Why Use Binary Numbers?
Easy to represent 0 and 1 using electrical values.
Possible to tolerate noise.
Easy to transmit data
Easy to build binary circuits.
AND Gate
1
0
0

## Slide 16: Conversion Between Number Bases
Decimal(base 10)
Octal(base 8)
Binary(base 2)
Hexadecimal
(base16)
to convert between
Learn bases.
Already demonstrated how to convert from binary to decimal.
Hexadecimal described in next lecture.

## Slide 17: General Base Conversion
Number Representation
Glven a number of radlx r of
and
“n”
inteqer digits an-1›• • •,a0
n
“m” fractional digits a 1,...,a m
written as:
an-1 an-2 an-3
has value: (Number) =
r
•• •
a2 a1 a0 • a-1 a-2 • ••
a-m
a
a, r'’
(Integer Portion)+ (Fraction Portion)

## Slide 18: Commonl
Occurrin
Bases
Name | Radix | Digits
Binary | 2 | 0,1
Octal | 8 | 0,1,2,3,4,5,6,7
Decimal | 10 | 0,1,2,3,4,s,g,7,8,9
Hexadecimal | 16 | 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
(= 0,1,2,3,4,5,6,7,8,9,10,11,12,13,14,15)

## Slide 19: Converting Binary to Decimal
To
Convert
to decimal, arithmetic to sum
use decimal the weighted
powers of two:
Converting 110102 to N10:
N10 = 1 x 24 x 1x 23 + 0 x 22 + 21 + 0 + 20
= 26

## Slide 20: Converting Decimal to Binary
Method 1 (Method 2 repeated division next slide)
  Subtract the largest power of 2 that gives a positive result and record the power.
  Repeat, subtracting from the prior result, until the remainder is
zero.
  Place 1’s in the positions in the binary result corresponding to the powers recorded; in all other positions place 0’s.
Example: 62510 4 1001110001,
625 — 512 = 113 4 9
’l’l3— | 64 = | 49 4 | 6
49 — | 32= | 17 6 | 5
17 — 1— | 16= 1= | ’I 44 061 | 
— Place 1’s in the the positions recorded and 0’s elsewhere
Converting biiiary to decimal: suni ›veiglsted powei's of 2 using
decimal arithmetic e.g., 512 + 64 + 32 + 16 + 1 = 625

## Slide 21: Conversion Between Bases
Convert the Integral Part
  Repeatedly divide the number by the radix you want to convert to and save the remainders. The new radix digits are th e remainders in reverse order of computation.
is the coe/ficie / of the radix's expo e /.
    If the new radix is > 10, then convert all remainders > 10 to digits A, B, . ..
Convert the Fractional Part
  Repeatedly multiply the fraction by the radix and save the integer digits that result. The new radix fraction digits are the integer numbers in computed order.
Why clo=s this '.+‘ork?
To convert fractional part. it should be divided by reciproca1 of radix. which is
same as multiplying with radix.
    If the new radix is > 10, then convert all integer num bers > 10 to digits A, B,
Join together with the racJix point

## Slide 22: Example: Convert 46.687510
To Base 2
Convert 46 to Base 2
'16/2 — 23
23/2 = 1 ’I
11/2 = 5
5/2 = 2
2/2 = 1
1/2 = 0
remainder — 0
remainder = 1
remainder = 1
remainder = ’I
remainder = 0
remainder= 1
Read off in reverse order: 10’I1102
Convert 0.6875 to Base 2:
0 6875 * 2 = 1 3750 int = 1
0 3750 * 2 = 0 7500 int = 0
U. /5UU ” ? = 1. t›UUU int = 1
0 ñ t00 * P = 1 0fJ0 I int = 1
0.0000
Read off in forward order. 0.10112
Join together with the radix point: 1011110.1011d

## Slide 23: Converting Among Octal, Hexadecimal, Binary
Octal (Hexadecimal) to Binary:
  Restate the octal (hexadecimal) as three (four) binary digits,
starting at radix point and going both ways
Binary to Octal (Hexadecimal):
  Group the binary digits into three (four) bit groups starting at the radix point and going both ways, padding with zeros as needed in the fractional part
  Convert each group of three (four) bits to an octal (hexadecimal) digit
Example: Octal to Binary to Hexadecimal
6 3 ? 1 7 7 8
= 1101 11|101 . 0011111|111 2
= 1|1001|1101 00111111111(000)2 (regrouping)
= 1 9 D 3 F 8. (converting)

## Slide 25: Number of Bits Required
Given M elements to be represented by a binary code, the minimum number of bits, n, needed satisfies the following relationships:
-- 2n y-- M • 2n -- 1
-- n -- ceiI(Iogi2M) where ceiI(x) is the smallest integer greater than or equal to x
Example: How many bits are required to represent
decimal digits with a binary code?
-- M = 10 n = 4

## Slide 26: Number of Elements Represented
Given n dig its in radix r, there are r" distinct elements that can be represented.
But, can represent m elements, m < W
Examples:
  Can represent 4 elements in rarlix r - 2 with n - 2 cligits: (00, 01,
10, 11)
  Can represent 4 elements in radix r = 2 with n = 4 digits: (0001,
0010, 0100, 1000)
    This code is caIled a "on e h ot" code

## Slide 27: Binary Codes for Decimal Digits
Decimal | 8,4,2,1 | Excess3 | 8,4,-2,-1 | Gray
0 | 0000 | 0011 | 0000 | 0000
2 | 0010 | 0101 | tillti | 01ti1
3 | 0011 | 0110 | 0101 | 0111
4 | 0100 | 0111 | 0100 | 0110
fi | 0101 | 1000 | 1ti11 | Otilti
6 | 0110 |  |  | 
7 | 0111 | 1010 | 1001 | 0001
There are over 8,000 ways that you can chose 10 elements from the 16 binary numbers of 4 bits. A few are useful:

## Slide 28: Binary Coded Decimal (BCD)
The BCD code is the 8,4,2,1 code.
This code is the simplest, most intuitive binary code for decimal digits and uses the same weights as a binary number, but only encodes the first ten values from 0 to 9.
Example: 1001 (9) = 1000 (8) + 0001 (1)
How many “invalid” code words are there*
What are the “invalid” code words?

## Slide 29: Excess-3 Code and 8, 4, —2, —1 Code
Decimal | Excess-3 | 8, 4, —2, —1
0 | 0011 | 0000
1 | 0100 | 0111
2 3 | 0101 0110 | 0110 0101
4 | 0111 | 0100
5 | 1000 | 1011
6 | 1001 | 1010
7 | 1010 | 1001
8 | 1011 | 1000
9 | 1100 | 1111
What property is common to these codes?
— These are reflected codes: complementing is performed simply by
replacing 0's by 1's and vice-versa

## Slide 30: Gray Code
Decimal | 8,4,2,1 | Gray
0 | 0000 | 0000
1 | 0001 | 0100
2 | 0010 | 0101
3 | 0011 | 0111
4 | 0100 | 0110
fi 6 | 0101 0110 | 0010 0011
7 | 0111 | 0001
8 | 1000 | 1001
9 | 1001 | 1000
What property does this Gray code have?
— Counting up or down changes only one bit at a time
(including counting between 9 and 0)

## Slide 31: Gray Code: Optical Shañ Encoder
011
ioo
B
000
010
00
000
100
10
(a) Binary Code for Positions 0 through 7 (b) Gray Code for Positions 0 through 7
Shaft encoder: Capture angular position (e.g., compass)
For binary code, what values can be read if the shaft
position is at boundary of “3” and “4” (011 and 100) ?
For Gray code, what values can be read ?

## Slide 32: Gray Code
Gray code is not a number system.
  It is an alternate way to represent four bit data
Only one bit changes from one decimal digit to the next
Useful for reducing errors in communication.
Can be scaled to larger numbers.
Digit | Binary | Gray Code
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0011
3 | 0011 | 0010
4 | 0100 | 0110
5 | 0101 | 0111
6 | 0110 | 0101
7 | 0111 | 0100
8 | 1000 | 1100
9 | 1001 | 1101
10 | 1010 | 1111
11 | 1011 | 1110
12 | 1100 | 1010
13 | 1101 | 1011
14 | 1110 | 1001
15 | 1111 | 1000

## Slide 33: Warning: Conversion or Coding?
Do NOT mix up conversion of a decimal number to a binary number with codinq a decimal number with a BINARY CODE.
1310 = 11012 (This is conversion)
13 <» 000110011 (This is coding)

## Slide 34: Binary Arithmetic
Single Bit Addition with Carry
Multiple Bit Addition
Single Bit Subtraction with Borrow
Multiple Bit Subtraction
Multiplication
BCD Addition

## Slide 35: Binary Addition
 | 1 | 1 | 1 | 1 | 0 | 1
+ |  | 1 | 0 | 1 | 1 | 1
1
0 1 0 0
1 0
Binary addition is very simple.
This is best shown in an example of adding two binary numbers…
1 1 1 1 1 1 carries
- - - - - - - - - - - - - - - - - -

## Slide 36: Binary Subtraction
1 |  |  | 10 | 
0 10 | 10 | 0 | 0 | 10
-
1 0 0 1 1 0 1
1 0 1 1 1
1 1 0 1 1 0
We can also perform subtraction (with borrows in place of carries).
Let’s subtract (10111)2 from (1001101)2…
borrows

## Slide 37: Binary Multiplication
Binary multiplication is much the
same except | as decimal that the | multiplication, multiplication |  |  |  | 
operations are much |  | simpler 1 0 1 |  |  | … 1 | 1
X |  | 1 |  | 0 | 1 | 0
0 |  |  | 0 | 0 | 0 | 0
1 0 |  |  | 1 | 1 | 1 | 
 | 0 | 0 | 0 | 0 | 0 |  | 
1 | 0 | 1 | 1 | 1 |  |  | 
1 | 1 | 1 | 0 | 0 | 1 | 1 | 0

## Slide 38: Error-Detection Codes
Redundancy (e.g. extra information), in the form of extra bits, can be incorporated into binary code words to detect and correct errors.
A simple form of redundancy is arit , an extra bit appended onto the code word to make the number of 1’s odd or even. Parity can detect all single-bit errors and some multiple-bit errors.
A code word has even parity if the number of 1’s in the code word Is even.
A code word has odd parity if the number of 1’s in the
code word is odd.

## Slide 39: 3-Bit Parit Code Exam ie
Fill in the even and odd parity bits:
Even Parit
Parit
00
001-
010-
011-
100-
101-
110-
Messa e.Pdrit
001
The binary codeword "1111" has even parity and the binary code "1110" has odd parity. Both could be used to represent data.

## Slide 40: Parity Codes
Parity codes are formed by concatenating a parity bit, P to each code word of C.
In an odd-parity code, the parity bit is specified so that the total number of ones is odd.
In an even-parity code, the parity bit is specified so that the total number of ones is even.
Information Bits
P
1 1 0 0 0 0 1 1

Added even parity bit
0 1 0 0 0 0 1 1

Added odd parity bit

## Slide 41: Parity Code Example
Concatenate a parity bit to the ASCII code for the characters 0, X, and = to produce both odd-parity and even-parity codes.
Character | ASCII | Odd-Parity ASCII | Even-Parity ASCII
0 | 0110000 | 10110000 | 00110000
X | 1011000 | 01011000 | 11011000
= | 0111100 | 10111100 | 00111100

## Slide 42: ASCII Code
Standard Code for Information
American Interchange
ASCII is a 7-bit code, frequently used with an 8th bit for error detection (more about that in a bit).
Character | ASCII (bin) | ASCII (hex) | Decimal | Octal
A | 1000001 | 41 | 65 | 101
B | 1000010 | 42 | 66 | 102
C | 1000011 | 43 | 67 | 103
… |  |  |  | 
Z |  |  |  | 
a |  |  |  | 
… |  |  |  | 
1 |  |  |  | 
‘ |  |  |  | 

## Slide 43: ASCiI Character Codes
American Standard Code for Information Interchange
This code is the most popular code used to represent
It uses 7-
information sent as character-based data. bits to represent:
94 Graphic printing characters.
34 Non-printing characters
Some non-printing characters are used for text format (e.g. BS = Backspace, CR = carriage return)
Other non-printing characters are used for record marhing and flow control (e.g. STX and ETX stai1 and end text areas).
ASCII is a 7-bit code, but most computers manipulate 8-bit quantity called byfe. To detect errors, the 8’h bit is used as a parity bit.

## Slide 44: ASCII Codes and Data Transmission
ASCII Codes
  A – Z (26 codes), a – z (26 codes)
  0-9 (10 codes), others (@#$%^&*….)
  Complete listing in Mano text
Transmission susceptible to noise
Typical transmission rates (1500 Kbps, 56.6 Kbps)
How to keep data transmission accurate?

## Slide 45: Overview
Hexadecimal numbers
  Related to binary and octal numbers
Conversion between hexadecimal, octal and binary
Value ranges of numbers
Representing positive and negative numbers
Creating the complement of a number
  Make a positive number negative (and vice versa)
Why binary?

## Slide 46: Understanding Binary Numbers
Binary numbers are made of binary digits (bits):
0 and 1
How many items does an binary number represent?
(1011)2 = 1x23 + 0x22 + 1x21 + 1x20 = (11)10
What about fractions?
(110.10)2 = 1x22 + 1x21 + 0x20 + 1x2-1 + 0x2-2
Groups of eight bits are called a byte
(11001001) 2
Groups of four bits are called a nibble.
(1101) 2

## Slide 47: Understanding Hexadecimal Numbers
Hexadecimal numbers are made of 16 digits: (0,1,2,3,4,5,6,7,8,9,A, B, C, D, E, F)
How many items does an hex number represent? (3A9F)16 = 3x163 + 10x162 + 9x161 + 15x160 = 1499910
What about fractions?
(2D3.5)16 = 2x162 + 13x161 + 3x160 + 5x16-1 = 723.312510
Note that each hexadecimal digit can be represented with four bits.
(1110) 2 = (E)16
Groups of four bits are called a nibble.
(1110) 2

## Slide 48: Putting It All Together
Binary, octal, and hexadecimal similar
Easy to build circuits to operate on these representations
to convert the three
Possible between formats

## Slide 49: Converting Between Base 16 and Base 2
3A9F16 = 0011 1010 1001 11112
3 A 9 F
Conversion is easy!
  Determine 4-bit value for each hex digit
Note that there are 24 = 16 different values of four bits
Easier to read and write in hexadecimal.
Representations are equivalent!

## Slide 50: Converting Between Base 16 and Base 8
Convert from Base 16 to Base 2
Regroup bits into groups of three starting from right
Ignore leading zeros
Each group of three bits forms an octal digit.
3A9F16 = | 0011 | 1010 | 1001 | 11112
 | 3 | A | 9 | F
352378 =
011 101 010 011 1112
3 5 2 3 7

## Slide 51: How To Represent Signed Numbers
Plus and minus sign used for decimal numbers: 25 (or +25), -16, etc.
For computers, desirable to represent everything as
bits.
Three types of signed binary number representations
: signed magnitude, 1’s complement, 2’s complement.
In each case: left-most bit indicates sign: positive (0) or negative (1).
000011002 = 1210
Sign bit
Magnitude
100011002 = -1210
Sign bit
Magnitude

## Slide 52: One’s Complement Representation
The one’s complement of a binary number involves inverting all bits.
  1’s comp of 00110011 is 11001100
  1’s comp of 10101010 is 01010101
For an n bit number N the 1’s complement is (2n-1) – N.
Called diminished radix complement by Mano since 1’s
complement for base (radix 2).
To find negative of 1’s complement number take the 1’s complement.
000011002 = 1210
Sign bit
Magnitude
111100112 = -1210
Sign bit
Magnitude

## Slide 53: Two’s Complement Representation
The two’s complement of a binary number involves inverting all bits and adding 1.
  2’s comp of 00110011 is 11001101
  2’s comp of 10101010 is 01010110
For an n bit number N the 2’s complement is (2n-1) – N + 1.
Called radix complement by Mano since 2’s complement for base (radix 2).
To find negative of 2’s complement number take the 2’s complement.
000011002 = 1210
Sign bit
Magnitude
111101002 = -1210
Sign bit
Magnitude

## Slide 54: Two’s Complement Shortcuts
Algorithm 1 – Simply complement each bit and then add 1 to the result.
Finding the 2’s complement of (01100101)2 and of its 2’s complement…
N = 01100101 [N] =
10011010
10011011
01100100
+
+ 1
---------------
10011011
1
---------------
01100101
Algorithm 2 – Starting with the least significant bit, copy all of the bits up to and including the first 1 bit and then complementing the remaining bits.
N = 0 1 1 0 0 1 0 1
[N] = 1 0 0 1 1 0 1 1

## Slide 55: Finite Number Representation
Machines that use 2’s complement arithmetic can represent integers in the range
-2n-1 <= N <= 2n-1-1
where n is the number of bits available for representing N. Note that 2n-1-1 = (011..11)2 and –2n-1 = (100..00)2
For 2’s complement more negative numbers than positive.
For 1’s complement two representations for zero.
For an n bit number in base (radix) z there are zn different unsigned values.
(0, 1, …zn-1)

## Slide 56: 1’s Complement Addition
Using 1’s complement numbers,
numbers is easy.
adding
to add
For example, suppose we wish
+(1100)2 and +(0001)2.
Let’s compute (12)10 + (1)10.
(12)10 = +(1100)2
(1)10 = +(0001)2
= 011002 in 1’s comp.
= 000012 in 1’s comp.
0 1 1 0 0
+ 0 0 0 0 1
0 0 1 1 0 1
0
0 1 1 0 1
Add carry
Final
Result
Step 1: Add binary numbers Step 2: Add carry to low-order bit

## Slide 57: 1’s Complement Subtraction
Step 1: Take 1’s complement of 2nd operand
Step 2: Add binary numbers
Step 3: Add carry to low order bit
Add carry
Final Result
1’s comp
Add
Using 1’s complement numbers, subtracting numbers is also easy.
For example, suppose we wish to subtract +(0001)2 from
+(1100)2.
Let’s compute (12)10 - (1)10.
(12)10 = +(1100)2 = 011002 in 1’s comp.
(-1)10 = -(0001)2 = 111102 in 1’s comp.
0 1 1 0 0
-
0 0 0 0 1
+
0 1 1 0 0
1 1 1 1 0
--------------
1 0 1 0 1 0
1
0 1 0 1 1

## Slide 58: 2’s Complement Addition
Using 2’s complement numbers, adding numbers is easy.
For example, suppose we wish to add +(1100)2 and
+(0001)2.
Let’s compute (12)10 + (1)10.
(12)10 = +(1100)2 = 011002 in 2’s comp.
(1)10 = +(0001)2 = 000012 in 2’s comp.
+
0 | 1 | 1 | 0 | 0
0 | 0 | 0 | 0 | 1
----------------
0 0 1 1 0 1
Final
Result
Step 1: Add binary numbers
Step 2: Ignore carry bit
Add
Ignore

## Slide 59: 2’s Complement Subtraction
0 | 1 | 1 | 0 | 0
0 | 0 | 0 | 0 | 1
Using 2’s complement numbers, follow steps for
subtraction
For example, suppose we wish to subtract +(0001)2
from +(1100)2.
Let’s compute (12)10 - (1)10.
(12)10 = +(1100)2 = 011002 in 2’s comp.
(-1)10 = -(0001)2 = 111112 in 2’s comp.
-
-----------------------
+
0 1 1 0 0
1 1 1 1 1
Final
Result
Step 1: Take 2’s complement of 2nd operand
Step 2: Add binary numbers
Step 3: Ignore carry bit
2’s comp
Add
-------------------------
1 0 1 0 1 1
Ignore Carry

## Slide 60: 2’s Complement Subtraction: Example # 2
Let’s compute (13)10 – (5)10.
(13)10 = +(1101)2
(-5)10 = -(0101)2
= (01101)2
= (11011)2
Adding these two 5-bit codes…
0 1 1 0 1
carry + 1 1 0 1 1
--------------
1 0 1 0 0 0
Discarding the carry bit, the sign bit is seen to be
zero, indicating a correct result. Indeed,
(01000)2 = +(1000)2 = +(8)10.

## Slide 61: 2’s Complement Subtraction: Example #3
Let’s compute (5)10 – (12)10.
(-12)10 = -(1100)2 = (10100)2
(5)10 = +(0101)2 = (00101)2
Adding these two 5-bit codes…
Here, there is no carry bit and the sign bit is
1. This indicates a negative result, which is what we expect. (11001)2 = -(7)10.
+
0 0 1 0 1
1 0 1 0 0
----------------
1 1 0 0 1

## Slide 62: Karnaugh Maps
Algebraic procedures:
  Difficult to apply in a systematic way.
  Difficult to tell when you have arrive data minimum solution.
Karnaugh map (K-map)can be used to minimize functions of up to 6 variables.
K-map is directly applied to two- level networks composed of AND and OR gates.
  Sum-of-products,(SOP)
  Product-of-sum,(POS).

## Slide 63: Minimum SOP
It has a minimum no. of terms.
  i.e, it has a minimum number of gates.
It has a minimum no. of gate inputs.
  i.e, minimum no. of literals.
  Each term in the minimum SOP is a prime implicant, i.e., it cannot be combined with others.
It may not be unique.
  Depend on the order in which terms are combined or eliminated.

## Slide 64: Minimum SOP
Example: vertical input scheme
1
1
2
2
3
4
3
Fan-in reduction

## Slide 65: Minimum POS
It has a minimum no.factors.
It has a minimum no.of literals.
It may not be unique.
  Use(X+Y)(X+Y’)=X
  Use(X+C)(X’+D)(C+D)=
(X+C)(X’+D)to eliminate term.

## Slide 66: Minimum POS
Example: Vertical input scheme

## Slide 67: 2-VariableK-map
Place1sand0sfromthetruthtablein the K-map.
Each square of 1s =minterms.
Minterms in adjacent squares can be combined since they differ in only one variable. Use XY’ + XY = X.

## Slide 68: 3-Variable K-map
Note BC is listed in the order of 00,01, 11, 10. (Gray code)
Minterms in adjacent squares that differ in only one variable can be combined using XY’ + XY = X.

## Slide 69: Location of Minterms
– Adjacent terms in3-variableK map.

## Slide 70: KMap Example
– K-map of F(a,b,c)=m(1,3,5)
=M(0,2,4,6,7)

## Slide 71: Place Product Terms on K Map
Example
– Place b,bc’ and ac’in the3-variableK map.

## Slide 72: More Example
Exercise.
Plotf(a,b,c)=abc’+ b’c + a’ into the K-map.

## Slide 73: SimplicationExample
Exercise.
Simplify:
F(a,b,c)=
m(1,3,5)
  Procedure: place minterms into map.
  Select adjacent1’singroupoftwo1’sor four1’setc.
  Kick off x and x’.

## Slide 74
(1()
l()
(a) Plot of minterms
I()
(1
l
(b) Simplified form of F

## Slide 75: More Example
The complement of F
  Usingfour1’stoeliminatetwovariables.

## Slide 76: Redundant Terms
If a term is covered by two other terms,that term is redundant. Thatis, it is a consensus term.
Example: yz is the redundant.

## Slide 77: More Than Two Minimum Solutions
F=m(0,1,2,5,6,7)

## Slide 78: 4-Variable K Map
Eachmintermisadjacentto4 terms With which it can combine.
  0,8 are adjacent squares
  0,2 are adjacent squares, etc.
  1,4,13,7 are adjacent to 5.

## Slide 79: Plot a 4-variable Expression
F(a,b,c,d)=acd+a’b+d’
acd= 1 if a=1, c=1,d=1

## Slide 80: Simplification Example
Mintermsarecombinedingroupsof2, 4,
or 8 to eliminate 1, 2, 3 variables.
Corner terms.

## Slide 81: Simplification with Don’t Care
Don’t care“x” is covered if it helps. Otherwise leave it along.

## Slide 82: Get a Minimum POS Using K Map
Cover 0’s to get simplified POS.
– We want 0 in each term.
5

## Slide 83: Determination of Minimum Expressions Using Essential Prime Implicants
Definitions:
  Implicants: An implicant of a function Fisasingle element of the onset(1)or any group of elements that can be combined together in a K-map.
  Prime Implicants: An implicant that cannot be combined with another to eliminate a literal.
  Essential Prime Implicants: If a particular element of the on-set is covered by a single prime implicant. That implicant is called an essential prime implicant.
All essential primes must be part of the minimized expression.

## Slide 84: Implicant of F
Implicant
  Any single1 or any group of1’s
Prime implicant
  An implicant that cannot be combined with another term to eliminate a variable.
    a’b’c,a’cd’, ac’are primeimplicant.
    a’b’c’d’isnot(combinedwitha’b’cd’). abc’ and ab’c’ are not.

## Slide 85: Prime Implicant
Asingle1 which is not adjacent to any Other 1’s.
Twoadjacent1’swhicharenotcontainedin a group of four 1’s. And so on.
  Shaded loops are also prime implicants, but not part of the minimum solution.
  a’c’d and b’cd are already covered by other group. So we do not need them.

## Slide 86: Essential Prime Implicants for Minimum SOP
If CD is chosen first, then f has 4 terms. We don’t need CD since it is covered by other group.CD is not a essential prime implicant.
m2 is essential prime implicant since it is covered only be one prime implicant. So does m5, and m14. We need them in the answer.

## Slide 87: Ruleof Thumb
Lookatallsquaresadjacenttoa minterm.
  If the given minterm and all of the 1’s adjacent to it are covered by a single term, then that term is an essential prime implicant
  But if it is covered by more than two prime implicant, we cannot tell whether this term is essential or not.
  The solution is A’C’+A’B’D’+ACD+ (A’BD or BCD).

## Slide 88: Flow Chart
Chap5
C-H26

## Slide 89: Example
Findthe1thatiscoveredbyonly one term first (Do not share with other circle).

## Slide 90: 5-VariableK Map
Usetwo4-variablemaptoforma5- variable K map (16 + 16 = 32) (A,B,C,D,E)
  A’in the bottom layer
  A in the top layer.

## Slide 91: 5Neighbors
Same plane and above or under

## Slide 92: Example:5-variables
Ans:F=A’B’D’ +ABE’+ACD+ A’BCE + {AB’C or B’CD’}
– P1+ P2 + P3 +P4 + AB’C or B’CD’

## Slide 93: One More
F=B’C’D’+B’C’E+A’C’D’+A’BCD+ ABDE + {C’D’E or AC’E}
(17,19,25,27=AC’E),(1,9,17,25=C’D’E)

## Slide 94: Simplification Using Map- Entered Variables
Extend K-map for more variables.
  When E appears in a square, if E=1, then the corresponding minterm is present in the function G.
  G(A,B,C,D,E,F)=m0+m2+m3+
Em5+Em7+Fm9+m11+m15+ (don’t care terms)

## Slide 95: Map-Entered Variable
F(A,B,C,D)= A’B’C + A’BC+
A’BC’D+ABCD+(AB’C),(don’t
care)
  Choose D as a map-entered variable.
  When D =0,F=A’C(Fig. a)
  When D =1,F=C+A’B(Fig. b)
    two1’sarechangedtox’ssincetheyare covered in Fig. a.
F= A’C+D(C+A’B)= A’C + CD + A’BD

## Slide 96: Combinational & Sequential Logic Circuits

## Slide 97: INTRODUCTION
In digital circuit theory, sequential logic is a type of logic circuit whose output depends not only on the present value of its input signals but on the sequence of past inputs, the input history as well. This is in contrast to combinational logic, whose output is a function of only the present input.

## Slide 98
Difference between combinational and sequential circuit. ...
Sequential circuits are those which are dependent on clock cycles and depends on present as well as past inputs to generate any output.
Combinational Circuit –
In this output depends only upon present input.
The sequential logic has memory while combinational logic does not.
They employ a feedback loop to give output back to input. Sequential logic circuits is a form of binary circuit; its design employs one or more inputs and one or more outputs.

## Slide 99
A combinational logic circuit performs an operation assigned logically by a Boolean expression or truth table.
Examples of common combinational circuits
include:
half adders,
demultiplexers, encoders
logic
full and
adders, multiplexers, decoders .

## Slide 100
A Sequential logic circuits is a form of binary circuit; its design employs one or more inputs and one or more outputs, whose states are related to some definite rules that depends on previous states. ... Examples of such circuits include clocks, flip-flops, bi-stables, counters, memories, and registers.
There are two types of sequential circuit, synchronous and asynchronous. Synchronous types use pulsed or level inputs and a clock input to drive the circuit(with restrictions on pulse width and circuit propagation). Asynchronous sequential circuits do not use a clock signal as synchronous circuits do.
Flip flop is a sequential circuit which generally samples its inputs and changes its outputs only at particular instants of time and not continuously. Flip flop is said to be edge sensitive or edge triggered rather than being level triggered like latches.

## Slide 101: Half adder
An adder is a digital circuit that performs addition of numbers. Half adder has only two inputs and two outputs. The half adder adds two binary digits called as augend and addend and produces two outputs as sum and carry; XOR is applied to both inputs to produce sum and AND gate is applied to both inputs to produce carry.
By using half adder, you can design simple addition with the help of logic gates.
Circuit Implementation
Truth Table
Block Diagram

## Slide 102: Why it is called as Half-adder ?
The half adder can add only two input bits (A and B) and has nothing to do with the carry if there is any in the input. So if the input to a half adder have a carry, then it will neglect it and adds only the A and B bits. That means the binary addition process is not complete and that's why it is called a half adder
How Half Adder works ?
Half adder is a simple combinational circuit used to add two single bits. It accepts two inputs and produce two outputs that is a sum output and a carry output. A half adder consists of two logic gates 1) XOR and 2) AND gate. And the carry operation performed by AND gate thus carry out put will be A+B.

## Slide 103: FULL ADDER
The full adder adds 3 one bit numbers, where two can be referred to as operands and one can be referred to as bit carried in. It produces 2-bit output and these can be referred to as output carry and sum.
The full-adder has three inputs and two outputs. The first two inputs are A and B and the third input is an input carry as C-IN. When a full-adder logic is designed, you string eight of them together to create a byte-wide adder and cascade the carry bit from one adder to the next.
Truth Table
Block Diagram
Circuit Implementation

## Slide 104
With the truth-table, the full adder logic can be implemented. You can see that the output S is an XOR between the input A and the half-adder, SUM output with B and C-IN inputs. We take C-OUT will only be true if any of the two inputs out of the three are HIGH.
So, we can implement a full adder circuit with the help of two half adder circuits. At first, half adder will be used to add A and B to produce a partial Sum and a second half adder logic can be used to add C-IN to the Sum produced by the first half adder to get the final S output.
If any of the half adder logic produces a carry, there will be an output carry. So, C-OUT will be an OR function of the half-adder Carry outputs.
The implementation of larger logic diagrams is possible with the above full adder logic a simpler symbol is mostly used to represent the operation. Given below is a simpler schematic representation of a full adder.

## Slide 105
A full adder is a digital circuit that performs addition. Full adders are implemented with logic gates in hardware.
A full adder adds three one-bit binary numbers, two operands and a carry bit. The adder outputs two numbers, a sum and a carry bit.
The Boolean expression for a full adder is as follows.
For the CARRY-OUT (Cout) bit: CARRY-OUT = A AND B OR Cin(A XOR B) = A.B + Cin(A ⊕ B)

## Slide 106: 4-Bit Parallel Binary adder :
A binary parallel adder is a digital function that produces the arithmetic sum of two binary numbers in parallel.
FOUR-BIT BINARY PARALLEL ADDER is a circuit in which two binary numbers each of n bits can be added by means of a full adder circuit. Consider the example that two 4-bit binary numbers B 4B 3B 2B 1 and A 4A 3A 2A 1 are to be added with a carry input C1.
A group of four bits is called a nibble. A basic 4-bit parallel adder is implemented with four full-adder stages as shown in Figure.

## Slide 107
Again, the LSBs (A1 and B1) in each number being added go into the right- most full-adder: the higher-order bits are applied as shown to the successively higher-order adders, with the MSBs (A4 and B4) in each number being applied to the left-most full-adder. The carry output of each adder is connected to the carry input of the next higher-order adder as indicated. These are called internal carries. In keeping with most manufacturers' data sheets, the input labeled C, is the input carry to the least significant bit adder; C4 in the case of four bits, is the output carry of the most significant bit adder; and ∑1 (LSB) through ∑4 (MSB) are the sum outputs. The logic symbol for 4-bit parallel adder is shown in Figure.
Two binary numbers each of n bits can be added by means of a full adder circuit. Consider the example that two 4-bit binary numbers B 4B 3B 2B 1 and A 4A 3A 2A 1 are to be added with a carry input C 1. This can be done by cascading four full adder circuits as shown in figure. The least significant bits A 1, B 1, and C 1 are added to the produce sum output S 1 and carry output C 2. Carry output C 2 is then added to the next significant bits A 2 and B 2 producing sum output S 2 and carry output C 3. C 3 is then added to A 3 and B 3 and so on. Thus finally producing the four-bit sum output S 4S 3S 2S 1 and final carry output Cout. Such type of four-bit binary adder is commercially available in an IC package.

## Slide 108: Half Substractor :
A half subtractor is an arithmetic circuit that subtracts two bits and produces their difference. The circuit has two inputs minuend (X) and subtrahend (Y) and two output bits, one is the difference bit (D) and the other is the borrow bit (B).
As like addition operation of 2 binary digits, which produces SUM and CARRY, the subtraction of 2 binary digits also produces two outputs which are termed as difference and borrow. The simplest possible subtraction of 2-bit binary digits consists of four possible operations, they are 0-0, 0-1, 1-0 and 1-1. The operations 0-0, 1-0 and 1-
1 produces a subtraction of 1-bit output whereas, the remaining operation 0-1 produces a 2-bit output. They are referred as difference and borrow bit respectively. This borrow bit is used for subtraction of the next higher pair bit.
So, we can define half subtractor as a combinational circuit which is capable of performing subtraction of 2-bit binary digits is known as a half subtractor. Here, the binary digit from which the other digit is subtracted is called minuend and the binary digit which is to be subtracted is known as the subtrahend.

## Slide 109
It performs the operation X – Y. It should be noted that the weight of the output borrow bit is -2, while the weight of the output difference bit is +1.
The truth table of the half subtractor is shown. The Boolean functions for the two outputs can be obtained directly from the truth table as:
D = (XY + XY) = X ⊕Y
The half subtractor boolean expressions are :
D = (X’Y + XY’) = X ⊕ Y
B = X’Y

## Slide 110: Full Substractor :
A full subtractor is a combinational circuit that performs a subtraction between two bits, taking into account that a 1 may have been borrowed by a lower significant bit. The circuit has three inputs and two outputs.
Input variables are minuend (X), subtrahend (Y), and previous borrow (Z); output variables are difference (D) and output borrow (B).
It performs the operation X – Y – Z. It should be noted that the weight of the output borrow bit is -2, while the weight of the output difference bit is +1. The truth table of the full subtractor is shown.
The full subtractor boolean expressions are :
(X’Y’Z + X’YZ’ + XY’Z’ + XYZ) = X ⊕ Y ⊕ Z
(X’Y’Z + X’YZ’ + X’YZ + XYZ) = X'(Y ⊕ Z) + YZ
•

## Slide 111
When there is a situation where the minuend and subtrahend number contains more significant bit, then the borrow bit which is obtained from the subtraction of 2-bit binary digits is subtracted from the next higher order pair of bits. In such situation, the subtraction involves the operation of 3 bits. Such situation of subtraction can’t handle by a simple half subtractor. So, combining two half subtractor we can form another combinational circuit which can perform this type of operation. This circuit is known as the full subtractor.
So we can define full subtractor as a combinational circuit which takes three inputs and produces two outputs difference and borrow. Above is the truth table of the full subtractor, we have used three input
variables X, Y
subtrahend
and Z which refers to the term minuend,
and borrow bit respectively. The two
outputs difference and borrow are named as D and B respectively.
The construction of full subtractor circuit diagram involves two half subtractor joined by an OR gate as shown in the above circuit diagram of the full subtractor. The two borrow bits generated by two separate half subtractor are fed to the OR gate which produces the final borrow bit. The final difference bit is the combination of the difference output of the first half adder and the next higher order pair of bits.

## Slide 112: Sequential Logic Circuits : FLIP-FLOPS :
Both Latches and flip flops are circuit elements wherein the output not only depends on the current inputs, but also depends on the previous input and outputs. The main difference between the latch and flip flop is that a flip flop has a clock signal, whereas a latch does not.
A flip-flop or latch is a circuit that has two stable states and can be used to store state information. A flip-flop is a bistable multivibrator. The circuit can be made to change state by signals applied to one or more control inputs and will have one or two outputs.
Latches and flip-flops are the basic elements for storing information. One latch or flip-flop can store one bit of information. The main difference between latches and flip-flops is that for latches, their outputs are constantly affected by their inputs as long as the enable signal is asserted. In other words, when they are enabled, their content changes immediately when their inputs change. Flip- flops, on the other hand, have their content change only either at the rising or falling edge of the enable signal. This enable signal is usually the controlling clock signal. After the rising or falling edge of the clock, the flip-flop content remains constant even if the input changes.

## Slide 113
There are basically four main types of latches and flip- flops:
SR, D, JK, and T. The major differences in these flip-flop types are the number of inputs they have and how they change state. For each type, there are also different variations that enhance their operations.
Each type can have different variations such as active high or low inputs, whether they change state at the rising or falling edge of the clock signal, and whether they have asynchronous inputs or not. The flip-flops can be described fully and uniquely by its logic symbol, characteristic table, characteristic equation, state diagram, or excitation table, and are summarized in Figure below.

## Slide 114: Flip-Flops : SR, D, JK, and T Flip-Flops

## Slide 115: S-R Latch using NAND & NOR Gate :
The bistable element is able to remember or store one bit of information. However, because it does not have any inputs, we cannot change the information bit that is stored in it. In order to change the information bit, we need to add inputs to the circuit. The simplest way to add inputs is to replace the two inverters with two NAND gates as shown in Figure. This circuit is called a SR latch.
In addition to the two outputs Q and Q', there are two inputs S' and R' for set and reset respectively. Following the convention, the prime in S and R denotes that these inputs are active low. The SR latch can be in one of two states: a set state when Q = 1, or a reset state when Q = 0.
Figure 4. SR latch: (a) circuit using NAND gates; (b) truth table; (c) logic symbol; (d) timing diagram.

## Slide 116: Continued…
Like the NOR Gate S-R flip flop, this one also has four states. They are
S=0, R=1—Q=0, Q’=1
This state is also called the SET state.
S=1, R=0—Q=1, Q’=0
This state is known as the RESET state.
In both the states you can see that the outputs are just compliments of each other and that the value of
Q follows the compliment value of S.
S=0, R=0—Q=Q0, & Q’ =Q0’ No change
If both the values of S and R are switched to 0, then the circuit remembers the value of S and R in their previous state.
S=1, R=1—Q & Q’= Remember
If both the values of S and R are switched to 1 it is an invalid state because the values of both Q and Q’ are 1. They are supposed to be compliments of each other. Normally, this state must be avoided.

## Slide 117: Continued
Another reason why we do not want both inputs to be asserted
i.e. R=S=1 is that when they are both asserted, Q is equal to Q', but we usually want Q to be the inverse of Q'.
Figure 5. SR latch: (a) circuit using NOR gates; (b) truth table; (c) logic symbol.

## Slide 118: S-R FLIP FLOP USING NAND GATE

## Slide 119: S-R FLIP FLOP USING NOR GATE

## Slide 120: Clocked S-R Flip-Flop :
The problems with S-R flip flops using NOR and NAND gate is the invalid state. This problem can be overcome by using a bistable SR flip- flop that can change outputs when certain invalid states are met, regardless of the condition of either the Set or the Reset inputs. For this, a clocked S-R flip flop is designed by adding two AND gates to a basic NOR Gate flip flop. The circuit diagram and truth table is shown below.
A clock pulse [CP] is given to the inputs of the AND Gate. When the value of the clock pulse is ‘0’, the outputs of both the AND Gates remain ‘0’. As soon as a pulse is given the value of CP turns ‘1’. This makes the values at S and R to pass through the NOR Gate flip flop. But when the values of both S and R values turn ‘1’, the HIGH value of CP causes both of them to turn to ‘0’ for a short moment. As soon as the pulse is removed, the flip flop state becomes intermediate. Thus either of the two states may be caused, and it depends on whether the set or reset input of the flip-flop remains a ‘1’longer than the transition to ‘0’ at the end of the pulse. Thus the invalid states can be eliminated.

## Slide 121: Clocked S-R Flip-flop

## Slide 122: J-K FLIP-FLOP :
JK flip-flops are very similar to SR flip-flops. The J input is just like the S input in that when asserted, it sets the flip-flop. Similarly, the K input is like the R input where it clears the flip-flop when asserted. The only difference is when both inputs are asserted. For the SR flip-flop, the next state is undefined, whereas, for the JK flip-flop, the next state is the inverse of the current state. In other words, the JK flip- flop toggles its state when both inputs are asserted. The circuit, truth table and the logic symbol for the JK flip-flop is shown in Figure 17.
Figure 17. JK flip-flop: (a) circuit; (b) truth table; (c) logic symbol.

## Slide 123: J-K Flip-Flop :
A J-K flip flop can also be defined as a modification of the S-R flip flop. The only difference is that the intermediate state is more refined and precise than that of a S-R flip flop.
The behavior of inputs J and K is same as the S and R inputs of the S-R flip flop. The letter J stands for SET and the letter K stands for CLEAR.

## Slide 124: J-K Flip-Flop :
When both the inputs J and K have a HIGH state, the flip-flop switch to the complement state. So, for a value of Q = 1, it switches to Q=0 and for a value of Q = 0, it switches to Q=1.
The circuit includes two 3-input AND gates. The output Q of the flip flop is returned back as a feedback to the input of the AND along with other inputs like K and clock pulse [CP]. So, if the value of CP is 1, the flip flop gets a CLEAR signal and with the condition that the value of Q was earlier 1. Similarly output Q’ of the flip flop is given as a feedback to the input of the AND along with other inputs like J and clock pulse [CP]. So the output becomes SET when the value of CP is 1 only if the value of Q’ was earlier 1.
The output may be repeated in transitions once they have been complimented for J=K=1 because of the feedback connection in the JK flip-flop. This can be avoided by setting a time duration lesser than the propagation delay through the flip-flop. The restriction on the pulse width can be eliminated with a master- slave or edge-triggered construction.

## Slide 125: D TYPE FLIP-FLOP :
Latches are often called level-sensitive because their output follows their inputs as long as they are enabled. They are transparent during this entire time when the enable signal is asserted. There are situations when it is more useful to have the output change only at the rising or falling edge of the enable signal. This enable signal is usually the controlling clock signal. Thus, we can have all changes synchronized to the rising or falling edge of the clock. An edge-triggered flip-flop achieves this by combining in series a pair of latches. Figure shows a positive edge-triggered D flip-flop where two D latches are connected in series and a clock signal Clk is connected to the E input of the latches, one directly, and one through an inverter. The first latch is called the master latch. The master latch is enabled when Clk = 0 and follows the primary input D. When Clk is a 1, the master latch is disabled but the second latch, called the slave latch, is enabled so that the output from the master latch is transferred to the slave latch. The slave latch is enabled all the while that Clk = 1, but its content changes only at the beginning of the cycle, that is, only at the rising edge of the signal because once Clk is 1, the master latch is disabled and so the

## Slide 126: Continued…
input to the slave latch will not change. The circuit of Figure 10(a) is called a positive edge-triggered flip-flop because the output Q on the slave latch changes only at the rising edge of the clock. If the slave latch is enabled when the clock is low, then it is referred to as a negative edge-triggered flip-flop. The circuit of Figure 10(a) is also referred to as a masterslave D flip-flop because of the two latches used in the circuit. Figure 10(b) and (c) show the truth table and the logic symbol respectively. Figure 10(d) shows the timing diagram for the D flip-flop.
Figure 10. Master-slave positive-edge-triggered D flip-flop: (a) circuit using D latches; (b) truth table; (c) logic symbol; (d) timing diagram.

## Slide 127: D type Flip-Flop :
The circuit diagram and truth table is given in figure
D flip flop is actually a slight modification of the above explained clocked SR flip-flop. From the figure you can see that the D input is connected to the S input and the complement of the D input is connected to the R input. The D input is passed on to the flip flop when the value of CP is ‘1’.
When CP is HIGH, the flip flop moves to the SET state. If it is ‘0’, the flip flop switches to the CLEAR state.

## Slide 128: T type Flip-Flop :
The T flip-flop has one input in addition to the clock. T stands for toggle for the obvious reason. When T is asserted (T = 1), the flip-flop state toggles back and forth, and when T is de-asserted, the flip-flop keeps its current state. The T flip-flop can be constructed using a D flip- flop with the two outputs Q and Q' feedback to the D input through a multiplexer that is controlled by the T input as shown in Figure 18.
Figure 18. T flip-flop: (a) circuit; (b) truth table; (c) logic symbol.

## Slide 129: T TYPE FLIP-FLOP :
This is a much simpler version of the J-K flip flop. Both the J and K inputs are connected together and thus are also called a single input J- K flip flop. When clock pulse is given to the flip flop, the output begins to toggle. Here also the restriction on the pulse width can be eliminated with a master-slave or edge-triggered construction. Take a look at the circuit and truth table is shown in figure.

## Slide 130: THANK YOU